## Slide 1
Unit-I
Water & It’s Treatment

## Slide 2
Organic Impurities: Organic impurities are decaying plant and animal matter. These impurities give water an unpleasant taste and odor.
Inorganic Impurities: These impurities include dissolved minerals, heavy metals ,pesticides, industrial pollutants, and pharmaceuticals.
Physical Impurities: These impurities include sediment, sand, rust, and debris, which affect water clarity and taste.
Total Dissolved Solids (TDS):TDS refers to the total concentration of dissolved minerals and salts in water. High TDS levels can lead to water that tastes salty or bitter.
Biological Impurities: Biological impurities include bacteria, viruses, and parasites. Consuming such water can lead to waterborne diseases.
Types of impurities in water

## Slide 3
Hard Water | Soft Water
Hard water does not lather with soap but instead forms a precipitate. | Soft water lather with soap.
Hard water doesn't form lather or foam with soap. | Soft water forms lather and foam with soap.
Soap is not effective against hard water. | Soap is effective against soft water.
Hard water has a characteristic taste and isn’t suitable for heavy machinery, boilers, and other appliances. | Soft water is known to have a salty taste and is widely suitable for machinery, boilers, etc.
Hard water is rich in minerals. Hence it mainly contains minerals such as magnesium and calcium. | Soft water is not rich in minerals. It mainly contains sodium ions.
Example: Water found in wells, groundwater | Example: rainwater
Difference between hard water and soft water

## Slide 4
The hardness of water
The total amount of dissolved calcium and magnesium salts present in the water is called hardness water.
Causes of hardness of water:
The presence of bicarbonates, chlorides, and the sulphates of calcium and magnesium in water causes the hardness of water.
Cations Ca2+ and Mg2+ present in hard water react with soap (sodium stearate) to form insoluble precipitates (calcium or magnesium stearate).
Lather will not be produced until all the calcium and magnesium ions are precipitated. Thus, it hinders the cleansing action of soap.
This also results in the wastage of a quantity of soap.
2C17H35COONa + CaCl2 → (C17H35COO)2Ca ↓ +2NaCl
Calcium Stearate
2C17H35COONa + MgSO4→(C17H35COO)2Mg↓ +Na2SO4
Magnesium Stearate

## Slide 5
Temporary hardness:
It is caused by the presence of dissolved bicarbonates of calcium and magnesium and carbonates of Iron.
Temporary hardness is easily removed by boiling, on boiling bicarbonates are decomposed into insoluble carbonates or hydroxides.
    Ca (HCO3)2 → CaCO3↓ + H2O + CO2↑
    Mg (HCO3)2 → Mg (OH) 2 ↓+ 2CO2↑
It is also known as carbonate hardness.
Types of Hardness

## Slide 6
It is caused by the presence of dissolved chlorides, and sulphates of the calcium and magnesium and iron.
The dissolved salts are CaCl2, MgCl2, CaSO4, MgSO4, FeSO4, Al2(SO4)3 etc.
Unlike temporary hardness, permanent hardness is not destroyed on boiling.
It is also known as non carbonate hardness.
Permanent hardness

## Slide 7
The hardness of water is expressed in terms of calcium carbonate equivalents.
The weights of different salts that causing hardness are converted to weight equivalent to that of calcium carbonate.
The reason for choosing CaCO3 as standard for reporting hardness is ease in calculations as its molecular weight is exactly 100 and is insoluble in water.
Degree of Hardness
Hardness causing salt and molecular weight
Ca(HCO3)2 = 162
Mg(HCO3)2 = 146
CaSO4 = 136
MgSO4 =120
CaCl2 = 110
MgCl2 = 95
CaCO3 =100

## Slide 8
Parts per million(ppm):-The number of parts by weight of CaCO3 present per million (106) parts by weight of water.
1ppm = 1 part of CaCO3 equivalents in 106 parts of water.
Degree Clarke(oCl):- Parts of CaCO3 equivalents of hardness per 70.000 parts of water.
1oCl = 1 part of CaCO3 per 70,000 parts of water.
Degree French(0Fr):- The parts of CaCO3 equivalents of hardness per 105 parts of water.
1oFr = 1 part of CaCO3 per 105 parts of water.
Milligram per litre
1 mg/lit = 1 mg of CaCO3 present in 1 lit of water
Relationship between units:
1 mg/lit = 1ppm = 0.07oCl = 0.1oFr
Units for Hardness

## Slide 9
Impurity | Ca(HCO3)2 | Mg(HCO3) | CaSO4 | MgSO4 | CaCl2 | MgCl2
weight | 4 | 8 | 6 | 5 | 10 | 12
Molecular weight | 162 | 146 | 136 | 120 | 110 | 95
A water sample on analysis is found to contain the following impurities. Calculate the temporary, permanent and total hardness of water in mg, ppm, oFr and oCl.
Solution
Ca (HCO3)2 and Mg (HCO3)2 cause temporary hardness
2.4 + 5.4=7.8 mg or ppm
7.8X0.07 = 0.546 oCl
7.8 x 0.1 = 0.78 oFr
CaSO4, MgSO4, CaCl2, and MgCl2, cause permanent hardness
4.4 + 4.1 + 9.0 + 12.6 = 30.1 mg (or) ppm
30.1 X 0.07 = 2.1 oCl
30.1 X 0.1 = 3.01 oFr
Total hardness = Temporary hardness + Permanent hardness
7.8 + 30.1 = 37.9 mg (or) ppm
37.9X 0.07 =2.65 oCl
37.9 X 0.1 = 3.79 oFr

## Slide 10
ESTIMATION OF HARDNESS OF WATER BY COMPLEXOMETRIC METHOD
PRINCIPLE:
The capacity of water to precipitate soap (prevent lather) is the hardness. It is caused by dissolved calcium and magnesium salts. Bicarbonates cause temporary hardness and chlorides and sulphates permanent hardness.
Ethylene diamine tetra acetic acid (EDTA) is a complexing agent, hexa-dentate ligand and forms complexes with Ca2+, Mg2+ ions. Hence the titration is complexometric titration. Eriochrome Black-T is the indicator and is blue in colour in Free State.

## Slide 11
When EBT is added to the hard water at pH = 10, it gives wine-red colored unstable complexes with Ca2+ and Mg2+ ions. The solution turns blue when this mixture is titrated against EDTA solution.

## Slide 12
Part-2
Standardization of EDTA
Pipette out 10ml. of Standard hard water into a conical flask. Add 5ml (approx.) of buffer solution and 2 to 3 drops of Eriochrome black-T indicator. The solution attains wine-red colour. Titrate the contents of the conical flask against the EDTA solution until the colour changes to blue. Note the burette reading and repeat the titration to get concurrent values.
N1V1 (Standard hard water) = N2V2 (EDTA)
Normality of standard hard water (N1) =
Volume of standard hard water (V1) = 10 ml.
Normality of EDTA (N2) =?
Volume of EDTA used in 2nd step (V2) =?
PROCEDURE
Part-1: Preparation of standard hard water
Take 0.01 grams of Epsom salt and transfer it into a 100 ml. standard flask. Add few ml. of distilled water and shake properly to get clear solution. Make up the solution up to the mark of the standard flask by adding distilled water.
Normality (N1) =
Normality (N1) =

## Slide 13
Part-3
Determination of total hardness of test sample of water
Pipette out 10ml. of test water sample into the conical flask. Add 5ml (approx) of buffer and 2 to 3 drops of Eriochrome Black-T indicator. The solution attains wine-red colour. Titrate the contents of the conical flask against EDTA solution till the colour changes from wine-red to blue. Note the burette reading and repeat the titration to get concurrent values.
N2V2 (EDTA) = N3V3 (Test water sample)
Normality of test water sample (N3) =
Volume of test water sample (V3) = 10 ml.
Normality of EDTA (N2) =?
Volume of EDTA used in 3rd step (V2) =?
The total hardness of the test sample of water is calculated as follows
Total hardness = N3 × 50 × 1000 = ----- mg/lit or ppm.
The total hardness of water is ------------ mg/lit or ppm.

## Slide 14
Part-4
Determination of Permanent hardness of test sample of water
Take 50ml of water in beaker , boil for 10 minutes and filter the water. Pipette out 10ml. of boiled test water sample into the conical flask. Add 5ml (approx) of buffer and 2 to 3 drops of Eriochrome Black-T indicator. The solution attains wine-red colour. Titrate the contents of the conical flask against EDTA solution till the colour changes from wine-red to blue. Note the burette reading and repeat the titration to get concurrent values.
N2V2 (EDTA) = N4V4 (boiled Test water sample)
Normality of boiled test water sample (N4) =
Volume of boiled test water sample (V4) = 10 ml.
Normality of EDTA (N2) =?
Volume of EDTA used in 4th step (V2) =?
The permanent hardness of the test sample of water is calculated as follows
Permanent hardness = N4 × 50 × 1000 = ----- mg/lit or ppm.
The total hardness = Permanent hardness + Temporary hardness.
Temporary hardness = The total hardness - Permanent hardness

## Slide 15
1.0 gm of Epsom salt was dissolved in 100 ml of distilled water. 50 ml of this solution required 45 ml of EDTA solution for titration. 50 ml of test hard water sample required 28 ml of EDTA and after boiling and filtering required 15 ml of EDTA solution. Calculate the total hardness, permanent hardness and temporary hardness of water.
Normality of St.HW (N1) =
=
N1V1 (St. HW) = N2V2 (EDTA) = 0.08 × 50 = N2 × 45, N2 = 0.088N
N2V2 (EDTA) = N3V3 (TWS) = 0.088 × 28 = N3 × 50, N3 = 0.049N
Total hardness = N3 × 50 × 1000 = 0.049 × 50 × 1000 = 2450 mg/lit (or) ppm.
N2V2 (EDTA) = N4V4 (boiled TWS) = 0.088 × 15 = N4 × 50 = 0.026N
Permanent hardness = N4 × 50 × 1000 = 0.026 × 50 × 1000= 1300 mg/lit (or) ppm.
The total hardness = Permanent hardness + Temporary hardness.
Temporary hardness = The total hardness - Permanent hardness = 2450- 1300 = 1150 mg/ lit (or) ppm

## Slide 16
The water supplied by municipality should be fit for human consumption.
It should satisfy the following requirements:
    It should be colorless, odourless, and pleasant to taste.
    Turbidity should not exceed 10 ppm.
    TDS should not exceed 500 ppm.
    It should not be very alkaline (pH 8.0).
    It should be free from dissolved gases.(H2S,CO2)
    It should be free from objectionable minerals such as Pb, As, Cs, Mn.
    It should be free from pathogenic organism.
Specifications of Potable or Domestic Water (WHO)

## Slide 17
Treatment of water for drinking purposes mainly includes the removal of suspended impurities, colloidal impurities and harmful pathogenic bacteria.
The following stages are involved in purification
        1. Screening
        2. Sedimentation
        3. Coagulation
        4. Filtration
        5. Disinfection
As required, other steps will be added, depending on the chemistry of the treated water.
Portable Water Treatment

## Slide 18
Screening
Screens remove large floating or suspended solids in the process of inflow. Materials like leaves, paper, twigs, and other debris are removed so as to avoid equipment or plant damage.
Aeration: The water is then subjected to aeration(reacting with air) which helps in exchange of gases between water and air, increases the oxygen content and removes the impurities like iron, manganese and dissolved gases like H2S, CO2 and NH3
Sedimentation : The process of removing big sized suspended solid particles from water is called as plain sedimentation. In this process, water is stored in big tanks for several hours. 70% of solid particles settle down due to force of gravity.

## Slide 19
Coagulation : This is the process of removing fine suspended and colloidal impurities by adding coagulants like potassium alum (K2SO4Al2(SO4)3 24H2O), Ferrous sulphate (FeSO4), Sodium aluminate (NaAlO2).
When coagulant is added to water, floc formation takes place due to hydroxide formation which can gather tiny particles together to form bigger particles and settle down quickly.
Filtration: The process of passing a liquid containing suspended impurities through a suitable porous material so as to effectively removed suspended impurities and some microorganisms is called filtration.
It is a mechanical process. When water flows through a filter bed, many suspended particles are unable to pass through the gaps and settle in the bed.

## Slide 20
Disinfection or sterilization: The process of killing pathogenic bacteria and other microorganisms is called disinfection or sterilization. The chemicals used for killing bacteria are called disinfectants.
Chlorination: The process of adding chlorine to water is called chlorination. Chlorine gas is a very good disinfectant, which can be bubbled in the water.
In this process calculated amount of chlorine gas is passed in order to destroy the pathogenic bacteria is called chlorination. Chlorine is also reacts with water and generates hypochlorous acid and nascent oxygen, which acts a powerful oxidizing agent and kills the bacteria
Cl2 + H2O → HCl + HOCl
Bacteria + HOCl → killed bacteria
Advantages:
    Storage requires less space, Effective and economical
    Produce no salts, Ideal disinfectant
Disadvantages:
    Excess of chlorine causes unpleasant taste and odour.
    More effective at below pH 6.5 and less effective at higher pH values.

## Slide 21
Break Point Chlorination (or) Free Residual Chlorination
Chlorination is one of the most common methods used in water treatment, primarily for disinfection.
During the process, Chlorine (Cl₂), Hypochlorous acid (HOCl), or Sodium hypochlorite (NaOCl) is added to water.
Apart from killing microorganisms, it can also help in removing or controlling some chemical impurities.
      Microbial Contaminants: Bacteria (E. coli, Salmonella, Vibrio cholera), Viruses (Hepatitis A, enteroviruses), Protozoa (Giardia and Cryptosporidium) and other pathogens.
      Organic Impurities: Organic matter (like phenols, hydrogen sulfide, and certain amines).
      Inorganic Impurities: Iron (Fe²⁺) , Manganese (Mn²⁺), Hydrogen sulfide (H₂S), Nitrite (NO₂⁻).
      Limitations: Chlorination does not remove dissolved salts (hardness, fluorides, nitrates, chlorides, sulfates, etc.). It may produce disinfection.

## Slide 23
The breakpoint chlorination curve explains what happens when chlorine is added to water containing ammonia and other reducing agents.
It is widely used in water treatment to understand chlorine demand, chloramine formation, and the point where free chlorine becomes available for effective disinfection.
    Zone-1 (Chlorine Demand): Chlorine is consumed by reducing agents such as iron, manganese, sulfide, and nitrite. No chlorine residual remains in the water. Chlorine is 'used up' neutralizing impurities.
    Zone-2 (Formation of Chloramines): Chlorine reacts with ammonia to form monochloramine. Some chlorinated organic compounds may also form. Combined chlorine residuals (chloramines) appear.
    Zone-3 (Chloramine Conversion & Nuisance Residuals): Additional chlorine converts monochloramine into dichloramine and nitrogen trichloride. Combined chlorine residuals start to decrease. These are considered nuisance residuals as they cause taste and odor problems.
    Zone-4 (Breakpoint Chlorination): At the breakpoint, all ammonia and chloramines are oxidized and destroyed. Beyond this point, free chlorine residuals (HOCl and OCl⁻) appear. Free chlorine is the most effective disinfectant.

## Slide 24
Breakpoint chlorination is the process of adding sufficient free chlorine to water to oxidize all reducing compounds and ammonia, thereby satisfying the water's chlorine demand and producing a free residual chlorine that acts as a potent disinfectant.
Impurity | Effect of Chlorination
1. Organic impurities (phenols, algae, odor compounds) | Oxidized, reducing taste and odor problems.
2. Iron (Fe²⁺) | Oxidized to Fe³⁺ and precipitated as ferric hydroxide.
3. Manganese (Mn²⁺) | Oxidized to MnO₂ precipitate.
4. Hydrogen sulfide (H₂S) | Oxidized to elemental sulfur or sulfate, removing foul odor.
5. Nitrites (NO₂⁻) | Oxidized to nitrates (NO₃⁻).
6. Bacteria, Viruses, Protozoa | Destroyed or inactivated by chlorine (disinfection).

## Slide 25
The Nalgonda Technique is a simple and widely used method for defluoridation of drinking (potable) water, developed by the National Environmental Engineering Research Institute (NEERI), Nagpur.
It is particularly suitable for rural and semi-urban areas in India where groundwater has high fluoride content.
PRINCIPLE: The technique works on the principle of chemical precipitation, adsorption, and coagulation–flocculation. Fluoride ions are removed by adding chemicals such as alum (aluminum sulfate), lime, and bleaching powder, which form insoluble complexes and settle along with suspended impurities.
Chemicals Used:
          1. Alum (Al₂(SO₄)₃·18H₂O) – acts as coagulant and precipitates fluoride.
          2. Lime (Ca(OH)₂) – aids in floc. formation and pH adjustment.
          3. Bleaching powder (Ca(OCl)₂) – disinfects the treated water.
Defluoridation of Potable Water by Nalgonda Technique

## Slide 26
Advantages
  Simple, low-cost, and easy to operate.
  Can be applied both at household & community level.
  Removes not only fluoride but also turbidity, color, and bacteria.
Limitations
  Requires accurate chemical dosing
  Generates sludge that needs proper disposal.
  May slightly change taste of water.
PROCESS STEPS:
Chemical dosing: Add the required amounts of alum, lime, and bleaching powder to the water.
Rapid mixing – Stir the water vigorously for a short time so the chemicals disperse uniformly.
Flocculation – Slow stirring helps in the formation of floc. which trap fluoride ions and suspended impurities.
Sedimentation – Allow water to stand undisturbed for a 1 hour, so the floc. settle at the bottom.
Filtration: Clear water is decanted or filtered to remove settled sludge.
Storage & supply: Defluoridated, and disinfected water is stored for drinking purposes.

## Slide 27
  Boilers are employed in industries for generation of steam.
  When raw water is directly feed into the boilers various physical changes and chemical reactions are induced in the boiler with the action of the heat.
  The ultimate result being the problem such as
      Caustic embrittlement and
      Sludge and Scale formation.
Boiler troubles

## Slide 28
Caustic Embrittlement
This is phenomenon during which the boiler material becomes brittle due to the accumulation of caustic substances.
During softening by lime-soda process, it is likely that some residual Na2CO3 is still present in the softened water.
In high pressure boilers Na2CO3 decomposes to give sodium hydroxide and CO2, and sodium hydroxide thus produced makes the boiler water “caustic”.
Na2CO3 + H2O 2NaOH + CO2
This caustic water flows into the minute hair-cracks, present in the inner side of boiler, by capillary action.
On evaporation of water the dissolved caustic soda concentration increases progressively which attacks the surrounding area, thereby dissolving iron of boiler as Sodium ferrate (Na2FeO2).
3 Na2FeO2 + 4 H2O 6NaOH + Fe3O4 + H2

## Slide 29
Further dissolution of iron takes place because of the precipitation of Fe3O4, and the regeneration of NaOH.
This causes embrittlement of boiler walls more particularly at stressed parts like bends, joints, rivets, etc., causing even failure of the boiler.
Caustic Embrittlement can be prevented:
By using sodium phosphate as softening reagent instead of sodium carbonate in external treatment.
By adding tannin or lignin to boiler water which blocks the hair-cracks in the boiler walls.
By adding sodium sulphate to boiler water. Na2SO4 also blocks hair-cracks.

## Slide 30
In boilers, water evaporates continuously and concentration of dissolved salts increases.
When it reaches saturation point they will be precipitated on the inner walls of the boilers.
If the precipitation takes place in the form of loose and slimy, it is called sludge.
If the precipitation takes place in the form of hard, adhering on the inner walls of the boilers, it is called scale.
2. Sludge & Scale formation

## Slide 31
Sludges | Scales
Sludges are soft loose and slimy precipitate. They are non-adherent deposits and can be easily removed. Formed by substances like CaCl2 , MgCl2 ,MgSO4, MgCO3 etc. Formed at comparatively colder portion of the boiler. They decrease the efficiency of boiler but are less dangerous. Can be removed by blow-down operation. | Scales are hard deposits. They sticks very firmly to the inner surface of boiler and are very difficult to remove. Formed by substance like CaSO4, Mg(OH)2 etc. Formed generally at heated portions of the boiler. Decrease the efficiency of boiler and chances of explosions are also there. Cannot be removed by blow-down operation.
Difference between Sludges and Scales

## Slide 32
Sludges are soft, loose, and slimy deposits that settle at the bottom of the boiler.
  It is formed at colder portions of the boilers.
  It is formed by substances, which have greater solubility in hot water than cold water(MgCO3,MgCl2, MgSO4, CaCl2).
  It can easily scrapped off with a wire brush.
Disadvantages:
      Reduce boiler efficiency
      Cause blockages in valves and pipelines
      Promote corrosion
Prevention of Sludge Formation:
    Blow-down operation (discharge of water from boiler bottom)
    Chemical treatment
    External water treatment (lime-soda, zeolite, ion exchange, demineralization)
SLUDGE

## Slide 33
Scales are hard, adherent, and crystalline deposits that stick firmly to the boiler walls. Scales may be formed inside the boiler due to:
A).Decomposition of Ca (HCO3)2:-In low pressure boilers CaCO3 causes scale formation, but high pressure boilers CaCO3 is soluble
                Ca (HCO3)2 → CaCO3↓ +H2O +CO2↑
                CaCO3 + H2O → Ca(OH)2 + CO2↑
B). Deposits of CaSO4:- The solubility of CaSO4 decreases with increasing the temperature. So it is soluble in cold water and insoluble in hot water. Hence it get precipitated in hotter region.
C). Hydrolysis of MgCl2:-
MgCl2 + 2H2O → Mg(OH)2 ↓ + 2HCl
D). Presence of silica:- Even if small quantity of SiO2 is present, it may deposits as CaSiO3 (or) MgSiO3. These deposits adhere very firmly on inner side of boiler surface.
SCALES

## Slide 34
Disadvantages of scale formation:
Wastage of fuel: Rate of heat transfer is greatly reduced due to poor conductivity of scales. Overheating is required for steady supply of heat hence fuel consumption increases.
Lowering of boiler safety: To supply steady heat overheating is required, which makes the boiler material weak &soft. Results in distortion of boiler tube.
Decrease in efficiency of boiler: Deposition of scales in valves and condensers choke them partially& decreases the efficiency of boiler
Danger of Explosion: Due to uneven expansion the thick scales gets cracked, results in formation of large steam & develops high pressure. It may cause explosion of boiler.
Removal of scales:
      Mechanical methods – scraping or wire brushing
      Thermal shocks – alternate heating and cooling
      Acid washing – dilute HCl or EDTA solution
      Conditioning – phosphate, carbonate, calgon, colloidal treatment

## Slide 35
  Water used for industrial purpose should be sufficiently pure.
  The process of removing hardness producing salts from water is known as softening of water.
  In industry, main methods employed for softening of water are two types.
                Internal treatment or conditioning
                External treatment or conditioning
Internal treatment:
The softening of water carried out inside the boiler is called internal treatment of water. In this process the hardness causing salts are removed
  Sludge formation can be removed by blow down operation.
  Scale formation can be prevented by internal treatment that involve addition of chemical to the boiler water either to precipitate or the scale forming impurities in the form of sludge.
Treatment (or) Softening of water for industry

## Slide 36
Colloidal conditioning:
    The scale formation in low pressure boilers can be prevented by the addition of kerosene, tannin, agar-agar etc.
    which will be get coated over the scale forming precipitates.
    These forms loose, non-sticky deposits (sludge) that can be removed by blow down.
    This type of conditioning is called colloidal conditioning.
Phosphate conditioning:
    In this process, the permanent hardness causing salts(Scale) in high pressure boilers will be removed by reacting with sodium phosphate.
    The complex formed is soft, non-adherent and easily removable(Sludge).
3MCl2 + 2Na3PO4 → M3( PO4)2↓ + 6NaCl
[Where M = Ca2+, Mg2+]
3MSO4 + 2Na3PO4 → M3 ( PO4)2↓ + 6NaSO4

## Slide 37
    C. Calgon conditioning:
        Sodium hexameta phosphate Na2[Na4(PO3)6 or (NaPO3)6 is called calgon.
        This forms soluble complex compounds with CaSO4.
        The treatment of boiler water with calgon is called calgon conditioning.
Na2 [Na4 (PO3)6] ↔ 2Na+ + [Na4 (PO3)6]2-
Calgon
2CaSO4 + [Na4 (PO3)6]2- → [Ca2 (PO3)6]2- + 2Na2SO4
Insoluble soluble insoluble

## Slide 38
The treatment given to water for the removal of hardness causing salts before it is taken into the boiler is called ‘external treatment’.
Ion exchange, de-ionisation (or) de-mineralization process:
Ion exchange resins are insoluble, cross-linked, long chain organic polymers with a micro porous structure, and the ‘active sites’ attached to the chains are responsible for the ion exchange properties.
Resins containing acid groups (COOH, SO3H) are capable of exchanging their H+ ions with other cations. This is called Cation exchange resin.
Ex: RCOOH, RSO3H
Resins containing basic groups (OH-, NH2-) are capable of exchanging their anions with other anions. This is called Anion exchange resin
Ex: R-CH2NMe2OH
External treatment:

## Slide 39
OH
Process:
The hard water is passed first through Cation exchange column, which removes the cations like Ca2+ and Mg2+ etc from it, and equivalent amount of H+ ions are released from the column to water.
2RH + Ca+2  R2Ca + 2H+
2RH + Mg+2  R2Mg + 2H+
After Cation exchange column, the hard water is passed through anion exchange column, which removes all the anions like SO42--, Cl -, CO23- etc. present in the water and equivalent amount of OH ions are replaced from this column to water.
ROH + Cl-  RCl + OH-
2ROH + SO4-2  R2SO4 + 2OH-
H+ and OH- ions (released from cation exchange and anion exchange columns respectively) get combined to produce water molecule.
H+ +OH-  H2O

## Slide 40
Regeneration :
Exhausted cation resin regenerated by dil. HCl , anion by dil.NaOH.
R2Ca + 2 H+  2RH + Ca+2 (washed)
R2SO4 + 2OH-  2ROH- + SO4-2(washed)
Advantages:
The process can be used to soften highly acidic or alkaline waters;
It produces water of very low hardness, say 2ppm.
So it can be used in high pressure boilers.
Disadvantages:
The cost of equipment is relatively high and also more expensive chemicals (resins) are needed.
Fe, Mn – containing water and turbid water cannot be treated because Fe and Mn are irreversibly exchanged and turbidity reduces the efficiency of the process.

## Slide 42
The process of removing common salt (sodium chloride) from water, is known as desalination.
The water containing dissolved salts with a peculiar salty (or brackish) taste, is called brackish water.
Sea water, containing on an average about 3.5% salts, comes under this category.
Brackish water is totally unfit for drinking purpose.
Commonly used methods for the desalination of brackish water is Reverse osmosis.
Desalination of brackish water

## Slide 43
When two solutions of unequal concentrations are separated by a semi permeable membrane, flow of solvent takes place from dilute to concentrated sides, due to osmosis.
If, however, a hydrostatic pressure in excess of osmotic pressure is applied on the concentrated side, the solvent flow reverses.
That is solvent is forced to move from concentrated side to diluted side across the membrane. This is the principle of reverse osmosis.
Reverse osmosis:

## Slide 44
Thus, in reverse osmosis method, pure solvent is separated from its contaminates, rather than removing contaminates from water.
This membrane filtration is sometimes also called super filtration or hyper-filtration
Advantages:
This process removes, ionic as well as non-ionic, colloidal and high molecular weight organic matter.
It removes colloidal silica, which is not removed by demineralization process.
The life time of membrane is quite high, about 2 years.
The membrane can be replaced within a few minutes, thereby providing nearly uninterrupted water supply.
Due to low cost, simplicity and high reliability, the reverse osmosis is gaining ground at present for converting sea water into drinking water.

## Slide 45
Short answer questions
List types of impurities in water.
Compare soft water with hard water.
Define brackish water and distilled water.
Differentiate Scales from Sludges.
What is desalination?
Write a not on reverse osmosis.
Define break point chlorination.
List specifications of portable water.
Define caustic embrittlement.
Compare temporary hardness with permanent hardness.
Write principle in EDTA method.
Define disinfection and give examples.
What are coagulants and give examples.
List salts causing temporary and permanent hardness.

## Slide 46
Long answer questions
What is hardness? Explain different types of hardness with units.
Elaborate ion exchange process with neat diagram and write limitations.
Explain various stages in the portable water treatment.
Describe the desalination of brackish water by Reverse Osmosis. Mention its advantages.
Illustrate caustic embrittlement.
Differentiate scales from sludges.
What is chlorination? Discuss break point chlorination.
Write a detailed notes scales and sludges.
Discuss internal water treatment.
Explain Defluoridation by Nalgonda Technique.